# SOPHISTICATED INSTRUMENTATION CENTRE

FOR APPLIED RESEARCH AND TESTING

(Sponsored by Department of Science & Technology, Govt. of India, New Delhi)                NABL Accreditated laboratory, Certificate No.T-5124

Sardar Patel Centre for Science & Technology

Charutar Vidya Mandal

Vallabh Vidyanagar – 388120, Dist ANAND, GUJARAT, INDIA

Phone: +91-2692-234966, Website: www.sicart.res.in

E-mail: sicart_cvm@hotmail.com , directorsicart@gmail.com

TENDER NOTICE

For the Purchase of ICP-OES (Inductive Coupled

Plasma-Optical Emission Spectrometer) iNSTRUMENT

| 1 | Last date for submission of tender | 10/12/2018 |
| --- | --- | --- |
| 2 | Date of opening of tender | Next working day at about 11.00 a.m from the closing date |
| 3 | Earnest Money deposit | 2 % of the total cost |
| 4 | Security Deposit | 5% of order value (before placing the PO) |
| 5 | Tender Fees (non – refundable) | Rs. 5,000/- Cheque or D/D in favour of “SICART- CVM” |

Tender Document Contains:

- Specifications

- General Terms & Condition

- Appendix

Dr. A. R. Jani

Hon. Director

SICART

CHARUTAR VIDYA MANDAL

VALLABH VIDYANAGAR – 388120

Dist: ANAND, GUJARAT

SOPHISTICATED INSTRUMENTATION CENTRE

FOR APPLIED RESEARCH & TESTING (SICART)

(Sponsored by Department of Science & Technology, Govt. of India, New Delhi)

NABL Accreditated laboratory, Certificate No. T - 5124

SARDAR PATEL CENTRE FOR SCIENCE & TECHNOLOGY

CHARUTAR VIDYA MANDAL, VALLABH VIDYANAGAR - 388120

Dist: Anand, Gujarat, India

Phone:(02692) 234966, Website: www.sicart.res.in

Email: sicart_cvm@hotmail.com, directorsicart@gmail.com

TENDER DOCUMENT FOR THE PURCHASE

OF

ICP – OES iNSTRUMENT

Dr. A. R. Jani

Hon. Director

SICART

CHARUTAR VIDYA MANDAL

SOPHISTICATED INSTRUMENTATION CENTRE

FOR APPLIED RESEARCH & TESTING (SICART)

(Sponsored by Department of Science & Technology, Govt. of India, New Delhi)

NABL Accreditated laboratory, Certificate No. T - 5124

SARDAR PATEL CENTRE FOR SCIENCE & TECHNOLOGY

CHARUTAR VIDYA MANDAL, VALLABH VIDYANAGAR - 388120

Dist: Anand, Gujarat, India

Phone:(02692) 234966, Website: www.sicart.res.in

Email: sicart_cvm@hotmail.com, directorsicart@gmail.com

TENDER NOTICE

Seal item rate tenders are invited from reputed and established manufacturers or authorized dealers for the supply, installation, testing and commissioning of ICP-OES Instrument & accessories having below specifications:

TECHNICAL SPECIFICATIONS:  The instrument shall confirm to the requirements of the specification including spares, accessories, and consumables as mentioned below in Part – A while Part - B is for other terms and conditions:

PART – A

- Scope :

The ICP spectrometer system should be a bench top model with compact size, able to determine trace and measure elements in diverse kind of samples like minerals, refractory, metals, Drugs and Pharmaceuticals, water and drinking water samples etc. System should be able to determine, major, minor and trace elements in single run measurement.  Fully PC controlled ICP-OES with following specifications. Complete system should have extensive safety & service diagnostic facility.

System should be capable to characterize in following modes / modules :

- Capable of handling even the most difficult, high-matrix samples without dilution, the system brings a whole new level of performance and flexibility to ICP.

- Unprecedented performance comes with unparalleled ease-of use. Unique hardware features and the industry’s most intuitive software combine to make multi-element measurements as easy as single-element analyses.

3.   The lowest argon consumption of any ICP (9ltr/min) or better.

4.   The fastest ICP startup (spectrometer ready in just minutes from power off)

5.   Superior sensitivity and resolution for all elements of interest

6.   The widest linear range with dual viewing technology

For the said purpose offers are invited from the reputed manufacturers / Representatives for supply, installation and commissioning of ICP-OES system. The system should meet minimum all the technical requirements as detailed below. The higher / advanced or any compatible version of any specification will also be considered if found suitable at the time of tendering.

- Technical Specifications:

| Sr. No. | Specifications | Detail |
| --- | --- | --- |
| 1 | Basic System configuration | The instrument must be DUAL VIEW (Radial and Axial) ICP-OES system, should be capable of addressing high matrices without the need of dilution or more compatible. The instrument must be equipped with polychromator or preferably dual monochromator for the best accuracy and precision or more compatible. Instrument should be equipped with Charge Coupled device (CCD) Detector/Charge injection Device (CID). The actual resolution (not the pixel resolution) of the system must be less than 0.009 nm at 200 nm or more compatible. System should have the maintenance free provision to remove the tail plume of plasma. System should be future upgradable to latest software. The system performance specifications listed below are indented to supplement the Vendor’s installation tests and are designed to ensure that the system supplied is able to meet the performance level required. These tests must be performed during installation, under a single set of tuning conditions: Detection limits based on three times the standard deviation of the blank. Long term stability, < 4% RSD over 4 hours Short term stability, <2% RSD over 20 minutes System should be upgradable in future for Halogen components like, Cl, Br, I and separate prices to be indicated for such upgradation & Laser Ablation system or more compatible. |
| 2 | Spectrometer | Spectrophotometer must cover full spectral range from 165-1100 nm or better. The system should include complete dual viewing optics under computer and software control. Any wavelength needed can be used in radial, axial or mixed viewing modes in a single run or more compatible. The entire optical system should be thermostatted or sealed and enclosed in a purged gas enclosure for low UV (160-190nm) performance required Gas purging for optics or more compatible. |
| 3 | RF generator | Free running solid state RF generator must run at frequency of 27.12 MHz or 40 MHz or in allied range with suitable power wattage adjustable from 800 to 1800 watts in 1 watt increment or more compatible. The power efficiency of Rf generator should be greater than 81% with < 0.1% variation in output power stability or more compatible. System should have the facility of online background correction or more compatible. |
| 4 | Argon gas consumption | System should have the least Argon gas consumption. (Please mention complete Argon consumption in L/min including Plasma, Auxiliary, Nebulizer, purging gas flows). System should have the least warm up time. (Please mention time in minutes from switching off from main switch to the first sample aspiration. Three replicates after the first aspiration should be demonstrated with satisfactory repeatability of the result). |
| 5 | Calibration Standard | NIST Standard Reference Material |
| 6 | Computer | A desk top PC should be provided for all operations of ICP-OES with minimum Core i5 or higher processor,8× DVD-RW drive facility,>500 GB HDD,>4 GB DDR RAM,21” LCD Monitor, Minimum 9 USB drives, Latest Windows operating system. A color laser printer shall be provided for graphic work. Other hardware’s (if necessary) |
| 7 | Chiller | Vendor should supply suitable Chiller re-circulator of appropriate capacity (if required) along with the system with warranty of minimum 05 year. |
| 8. | Other accessories | Auto sampler. Brine Analysis kit (for Brine samples), Organic sample kit (with ultrasonic Nebulizer) and FIAS kit ( for hydride elements). Hydride generator kit should also be included for hydride forming elements like As, Hg, Se. In main item. Suitable Fume exhaust system should be quoted. Other accessories like air compressor, Argon cylinders (qty 4), nitrogen cylinders (qty )2 having suitable dual stage regulator and purification pannels should also be included. |
| 9. | Installation qualification, Operational qualification, Procedural qualification (IQ,OQ,PQ) | As per NABL, IQ, OQ, PQ documentations are required at the time of installation of the instrument. |
| 10. | Warranty | Five Years (The Spares and support from the supplier should be available for 7 or more years after warranty). All the warranty replacement parts will be dispatched on DDP basis |
| 11 | UPS | Minimum 20 KVA on line branded appropriate UPS to run ICP-OES system with 30 minutes backup. |
| 12 | Manual | 2 set of Operation and maintenance manuals in English language should be supplied along with the system. |
| 13 | Performance Guarantee | System should be guaranteed for better accuracy. The accuracy of each element on wavelength should be equal or better than based on the internationally accepted Standard Reference Material by NIST. |
| 14 | Training | Necessary training to 3 persons of SICART staff on Operation, Maintenance, Calibration of the offered system and Instrument studies will have to be provided at customer’s site and Company’s Application centre. |
| 15 | After Sales Service Support | The vendor offering the required ICP-OES system should have their service centre in India preferably in Gujarat / Maharashtra such that the engineer can attend any service call within 48 hours. |
| 16 | Essential Spares and Consumables | Tool kit with all mechanical tools and accessories for the system installation and regular operation should be provided. Necessary spares and consumables required for smooth and efficient operation of ICP-OES for 10 years should be quoted. |

PART – B

♣ GENERAL Conciliations of Supply:

1. The instrument and all its sub units should operate on 230 ±10 volts, 50 Hz power

supply.

2. All the operations and maintenance manuals, circuit diagrams, application notes

and application software to be supplied should be in English language.

3. The supplier/ manufacturer shall have to arrange for after sales service as well as

O & M through their Indian agent/ representative to be specifically nominated in their bid proposal. However, the purchaser will place a single order in the name of bidder and no separate order in the name of the Indian Representative/ Agent will be placed for after sales/ O & M service.

4. The main unit and all the sub units of the instrument should be serviced by the

Indian representative supplier.

5. Bidders shall invariably furnish documentary evidence in the form of client’s

certificate In support of satisfactory supply and operation of the equipment as

mentioned in the qualification requirement.

6. Notwithstanding anything stated above the purchaser reserves the right to assess

the capability and capacity of the bidder to perform the contract, should the

circumstances warrant such as assessment in the overall interest of the

purchaser.

7. Comprehensive warranty with free of cost supply of spares for 05 years from the

date of successful commissioning of the instrument should be covered. Also, after

five years warranty, extended warranty up to 2 years to be covered separately if

asked for.

8. The maximum down time period for repairs of the equipment shall be 72 hours

from the date of notification by the purchaser to the bidder/supplier.

- Installation of the instrument and performance demonstration must be made at site.

- Onsite warranty at least for five years after the date of satisfactory installation.

- Training for at least three persons at site for learning the basic operations.

- Invoice should have the costing of each unit /component of ICP-OES Instrument separately.

- Principal should submit the compliance certificate at the time of installation.

(9) General Points:

SUPPLIERS PARTICULAR

Name of the firm 					:

Whether sole Proprietor Partnership/		:

Pvt. Ltd/Public Ltd under Indian

Company’s Act, 1956.With copy of

Partnership Public Ltd., Regn. Certificate.

Name of sole Proprietor or managing

Partners or Managing Director and other

Directors with addresses, telephone		:

Numbers and Email IDs

Details of registered office and other

Regional Offices

Contact persons for matters as regards

The present contract(Legal authority may

be cited)						:

APPENDIX – I

INFORMATION TO BE PROVIDED BY

THE SUPPLIER / INDIAN REPRESENTATIVE OF FOREIGN CO.

WITH THE QUOTATION

- Details of the infrastructural requirements (including glassware, chemicals and gases & standard)s for the installation of the system being offered.

- Details of the sales/service facilities.

  - Location of the sales/service facilities.

  - Number of the Service Engineer at each center with their existing servicing load (in terms of the number of units being serviced.)

  - List of details of the spaces which are available (in case of foreign manufacturers only) with the Indian representative for providing quick maintenance of the unit.

- Details of the training facilities available.

  - Location of centers

  - Types of the training programmers offered with syllabus.

  - Details of training aids available

  - Charges for training programme

- Details information about the application lab facilities available ---------

- Information about the development of the system

  - Year of introduction and expected life of the model being offered

  - Expected year in which the model being offered will be out of production.

- Any other information the tenderer wished to supply

- Details about the organizations in India where similar unit / Instrument is supplied and is in working condition.

SOPHISTICATED INSTRUMENTATION CENTRE

FOR APPLIED RESEARCH & TESTING (SICART)

(Sponsored by Department of Science & Technology, Govt. of India, New Delhi)

NABL Accreditated laboratory, Certificate No.T-3243

SARDAR PATEL CENTRE FOR SCIENCE & TECHNOLOGY

CHARUTAR VIDYA MANDAL, VALLABH VIDYANAGAR - 388120

Dist: Anand, Gujarat, India

Phone:(02692) 234966

Email: sicart_cvm@hotmail.com, Website: www.sicart.res.in

General Terms and Conditions

- The rates should be quoted for each item, stating the specific Brand / Make / Model no. etc. with taxes. The bidder must quote for the equipment in accordance with the specifications mentioned in the tender document which is forming a part of the contract.

The bidders, nevertheless, may submit the offer for similar compatible equipment under the head “option:” and quote separately for such similar equipments or accessories. The price may also be quoted in foreign currency i.e Dollar, Pound, Euro etc. by authorized representatives of imported equipment.

- The rates should be inclusive of all taxes FOR destination at the institute and should be quoted in the following format.

  - Basic prices of the Unit --------------------------------

  - Price of necessary accessories / spares / chemicals / glassware’s etc. with detailed specifications to be supplied with basic unit and for optional.

  - Taxes

-	GST -	___________________________

-	ST	-	___________________________

-	Octroi	-	___________________________

  - Packing and Forwarding _____________________

  - Mode of Transport for (Delivery at Vallabh Vidyanagar, Dist: Anand in Gujarat) _________________

  - Installation and Commissioning & Training _________________________

  - Total

  - The total price for each item as delivered in 2.7 above should be quoted in bill of material.

- The Purchaser being educational institute, the concessions applicable in rates / taxes under State / Central Government notification should be considered while quoting. The institution cannot issue C & D Forms / Certificates which may please be noted. The institution can, however, issue a certificate that the equipment being procured would be used exclusively for teaching / research purposes.

- Conditional tender shall not be accepted.

In case of the authorized dealers quoting on behalf of manufacturers, a copy of certificate stating that the equipment is being quoted by the party is on behalf of the concerned manufacturer and manufacturer undertake the responsibility to provide the after sales maintenance of the equipment.

- The supplier should clearly state the delivery period and time period required for installation and commissioning of the equipment, from the date of receipt of firm order. But it should be 12 weeks from the date of opening of the LC ( 8 weeks from the date of the purchase order for Indian suppliers) or equivalent commitment. In case, if supplier anticipates delay in delivery of any or all items due to the reasons beyond his control, the supplier shall apply for suitable extension stating the reason for the same and state its confirm date of delivery. The purchaser, if feels suitable may extend the delivery date.

- In case of delay of delivery of the equipment beyond the stipulated period, a penalty of 5% (Five Percent) of the total value of the ordered equipment will levied for each of delay or part thereof. The maximum penalty however shall not exceed 25% of the ordered value.

- The supplier or the Indian representative should install the system and bring in to complete operation, at Vallabh Vidyanagar in Gujarat on a location of the purchaser’s choice and to satisfaction, without any charge.

- The supplier or the Indian representative should give performance warranty for (i) the Complete system for five years from the date of the completion of the satisfactory installation and commissioning (ii) list of critical and non critical spares (iii) and service back up including commitment for the availability of the spares, of the system for a period of minimum 10 years from the date of installation. Also in case of equipment going out of production, at least two years advance notice should be given to enable, one time procurement of the spares

- Demonstration and training for operators of all modules. This should include (besides standard samples,) the satisfactory analysis of at least (5) SICART samples carried out by SICART Scientists. Minimum four training may be provided, three at our site and one at your application center until the user satisfy with training.

- The supplier shall arrange for repair / replace the defective / worn out components, of the equipment at our place during the guarantee period at purchaser’s first instructions within 10 (Ten) days. This will be carried out at the cost of supplier and no charges whatsoever will be paid including the T.A and D.A of the service engineer for the same.

- In the event of material supplied are not being in accordance to the specifications of items ordered, the supplier will bear the cost and risk, arrange to replace the same without any claims whatsoever for the same.

- In case the quoted rates are as per the valid and prevailing contract with DGS and D, New Delhi, the supplier shall furnish certified photocopy of the same to the purchaser. It may also be mentioned whether supplier can accept a direct order based on DGS and D rate Contract.

- The tender, as quoted once shall be considered final. No change, alterations and modifications shall as permitted at a later stage. Incomplete or unsatisfactory tenders will be rejected without assigning any reason thereof.

- The supplier shall provide user’s list and the certificates of satisfactory operation / compliance certificate of the equipment from few organizations to whom the similar equipment has been supplied in the recent past preferably in the Gujarat region.

- The validity of the tender may be kept open for a minimum period of 270 days after the receipt of the quotation which may further be extended if need arises.

- The earnest money: The tender copy dully filed in must accompany a Crossed Demand Draft for 2% of the total cost in favor of “SICART - CVM” payable at Vallabh Vidyanagar/ Anand. This money shall be refunded to the unsuccessful dealer, as far as possible within 60 days from the date of the opening of the tenders; no interest shall be paid on earnest money deposited. Any offer received without the EMD shall stand wholly rejected. Nevertheless, CVM’s decision by its authority on such matter shall remain final and binding.

- The supplier shall provide both technical service manual and operation / installation manual along with the dust cover for the equipment free of cost.

- Payment

- Advance payment will not be made.

- 70% of the total amount will be paid on supply of equipment after checking for specifications and installation and successful commissioning of the equipment. In a case where the equipment has not been found in conformity of the specifications as per the final purchase order, the same shall stand rejected. No case of any kind thereof should be paid by the owner

- Remaining 30 % of the amount will be paid after 3 months from the date of installation and successful operation of the equipment.

- The supplier will be required to get instrument serviced twice in a year for its

Satisfactory operation during the guarantee period of five years. Necessary calibration of the instrument will be done by the supplier as and when required. Separate rates for the calibration shall be quoted along with the period of calibration required.

20.0	The authority of CVM reserves all the rights to increase or decrease the quantity of or split of the items of the tender at any time while finalization of the award.

- The CVM authority also reserves the right to reject any or all of tenders without

assigning Any reasons thereof.

- In case of any dispute the Jurisdiction shall be ANAND.

- The  tender   for   equipment   must   be   sent   in   sealed   envelope  with  the

Superscription “TENDER FOR ICP- OES Instrument for SICART” and addressed to Hon. Director, SICART, Charutar Vidya Mandal, Mota Bazar, Vallabh Vidyanagar - 388120, Dist: Anand (Gujarat), India.

- Tenders received late shall not be accepted. All  tenders shall be opened in

presence of the bidders in the office of SICART in  accordance with the date &

time specified in the tender notice. The tenders will be opened on next working

day at about 11.00 a.m from the closing date.

25.0  Additional information per appendix-I should be provided along with the tender.

26.0   Please  also  certify in  the  quotation  that the price quoted are as laid down in

the Manufacturers/sole distributor’s price list.

27.0  Any special discount for educations/research institution should be specified.

- The manufactures printed leaflet, technical literature of specifications of every

item quoted should be accompanied with the quotation failing which quotations

will be Summarily rejected.

29.0   Pre- installation requirements such as power requirement (single phase or

three phase, Power load) Cooling water supply, air compressor ,air condition

machine etc. if any) should be provided and specified.

30.0    In case of items costing more than 1.0 lakh, firm whose quotation shall be

accepted,  shall  have  to  give  an  affidavit/declaration  on non-judicial stamp

paper,  to  be  signed   before   competent   magistrate  for  installation,   free

warrantee   service  during  warranty  period,  for  assurance  for the supply of

spare   parts,   components   on   payment   basis   and   also   for   refund   or

adjustment  of  payment  against  advanced  payment  made.

- (a)   In  case  of  imported  instruments  the  dealers  will  be  required to deposit

Rs. 1 lakh or  5%  value   of   the  order  (Whichever is more)  with  SICART

before order  is  placed  to  the  Dealers  and before opening of

Irrevocable  LC or other competent option of payment. This amount   is to be

held as security deposit without

any interest.  The amount will be refunded without interest to Dealers as

and when  instruments  are  satisfactory   installed  and   demonstrated  as

per specifications and on receipt of all the service manuals.

(b)  A performance Bank guarantee of 5% value of the instrument/equipment

is to be given, valid for two years as per the format provided.

32.0   FORFEITURE OF SECURITY DEPOSIT CLAUSE FOR IMPORTED ITEMS

- No change in items and conditions of dealer’s will be permitted once the LC is opened or mode of payment is decided. If  due  to a  default  on  the  dealer’s  part  the  LC lapses or is to be cancelled, than the security deposit of the dealer will be forfeited, in addition to it the dealer will be liable for payment  of  excess  amount  (more  than  the security deposit) spent on opening of the LC or other related expenses.

- If the imported instrument is not installed properly within the stipulated time                 and/or the service manuals are not provided within the stipulated time, the                 security deposit will be forfeited.

33.0     No correspondence queries or reminders or personal visits regarding quotation

position or ordering action will be entertained or replied. Orders when finalized

will be intimated to the parties concerned ONLY.

34.0	Before  placing  the  orders,  we  may  ask  the  dealers/ suppliers  to  give us the demonstration of   their  equipment/instrument   at   their   factory   or other  laboratories. They have to make all the necessary arrangements for the same.

Note :  1. The tender may be accompanied with an undertaking from the party/supplier

that the terms and conditions of the tender are accepted to and binding on the Party/supplier.

2. Please return this copy of terms and conditions duly signed and stamped

along with the tender documents.

Name of the Supplier:

Signature of the Supplier   :

Office Stamp                 :